## Slide 1: SPREAD SPECTRUM TECHNIQUES
BY
ANAND S.KHAIRE
EE 650

## Slide 2: What is a Spread Spectrum?
Spread Spectrum is a means of transmission in which the signal occupies a bandwidth in excess of the minimum necessary to send the information. The band spread is accomplished by means of a code which is independent of the data ,and synchronized reception with the code at the receiver is used for de-spreading and subsequent data recovery.

## Slide 3: Why Bother?
Advantages of Spread Spectrum:
Anti-jamming (A/J).
Anti-interference (A/I).
Low Probability of intercept (LPI).
Code Division Multiple Access (CDMA).
Message Privacy

## Slide 4: Spread Spectrum Techniques and Technology
Spectrum Spreading Techniques
Processing Gain
Jamming Margin

## Slide 5: Spectrum Spreading Techniques
Direct Sequence (DS)
Frequency Hopping (FH)
Time Hopping (TH)
Hybrids (Simultaneous frequency hopping and direct sequence modulations, simultaneous time hopping and direct sequence modulation and simultaneous time and frequency modulation)

## Slide 6: Process Gain
Process gain is a readily available quantity ,if the bandwidth employed in a system is known and the information rate is available.
Process Gain Gp= BW RF / R info.
A spread spectrum system develops its process gain in a sequential signal bandwidth spreading and de-spreading operation.

## Slide 7: Jamming Margin
It is observed that the processor cannot perform with the same efficiency when it faces an interfering signal having power level greater than the desired signal
Jamming margin expresses the capability of a system to perform in such a hostile condition.This quantity is usually intended in the specification of SS system but is less predictable from bandwidth and the information rate.
Jamming Margin= Mj=Gp-[ Lsys + (S/N)out ]
where Lsys=system implementation loss
(S/N)out=signal-to-noise ratio at the information output.
The “Jamming Threshold” of a particular system is of interest in determining how well the system will perform in the presence of interference.

## Slide 8: DS Spread Spectrum System
Direct Sequence is widely used for spread spectrum communication. It is nothing but the modulation of a carrier by a code sequence.
At the transmitter the spreading is obtained with the help of balanced modulator using the PN-code generator along with the carrier and data.
Although other modulation forms such as PAM could be used, balanced modulation is most common in direct sequence system.

## Slide 9: DS Spread Spectrum

## Slide 10: Overall Direct Sequence System

## Slide 11: DS concept ,before and after despreading.

## Slide 12: Balanced Modulation in DS Spread Spectrum
Suppressed Carrier produced is difficult to detect without resorting to somewhat sophisticated methods.
More power is available because the transmitter power is used to send only the code produced signal.
The PAM modulation also produces a (Sin x/x)² power spectrum but lacks same effective power at the receiver.

## Slide 13: Noise Reduction Using the DSSS system
At the receiver,after amplification the received signal is multiplied by a reference with the same code and assuming that the transmitter and receiver code are synchronous the original carrier is recovered.
Similarly the undesired signals are also processed in the same process of multiplication by the receivers reference that maps the received direct sequence signal into the original carrier bandwidth
Now since the unsynchronized input signal is mapped into a bandwidth at least as wide as receivers reference,the BPF can reject almost all the power of an undesired signal.

## Slide 14: Direct Sequence Process Gain
Process Gain Gp= BW RF / R info.
The usual assumption taken is that the RF bandwidth is that of the main lobe of [Sin x/x]2 direct sequence spectrum,which is 0.88 times the bandwidth spreading clock rate.
Therefore for a system having a 10Mcps clock rate and a 1Kpbs information rate the process gain is
(0.88*107 )/(1*103)=8.8*103 or 39dB

## Slide 15: Frequency Hopping Technique
“Frequency Hopping” modulation is more accurately termed as “multiple frequency,code selected ,frequency shift keying”.
A frequency hopping system or “Frequency Hopper” basically consists of a code generator and a frequency synthesizer capable of responding to the coded output from the code generator.

## Slide 16: Basic Frequency Hopping System

## Slide 17: Frequency hopping concept

## Slide 18: How does a “Frequency Hopper” work?
Frequency hopper is nothing more than a FSK,only the set of frequency choices is greatly expanded.
The input signal is generated using the pseudo noise generator and a frequency synthesizer.Thus the output of this setup varies according to the pseudorandom noise.
The received signal is mixed with locally generated replica,which is offset a fixed amount such that {f1,f2,……..fn}*{f1+IF,f2+IF,…….fn+IF} is produced with a constant difference frequency f IF.

## Slide 19: Noise reduction using the FH system
As in the DSSS system any signal that is not the replica of the local reference is spread by multiplication with the local reference.Same thing is observed in the frequency hopping system also .
Bandwidth of an undesired signal after multiplication with the local reference is again equal to the covariance of the two signals.
A signal with the same bandwidth as the local reference would have twice the reference bandwidth.The IF filter then can reject all the signal power that lies outside its bandwidth.

## Slide 20: How do we determine the frequency hopping rate?
The minimum frequency switching rate usable in a frequency hopping system is determined by a number of parameters:
The type of information being sent and its rate.
The amount of redundancy used,if any.
Distance to the nearest potential interferer.

## Slide 21: How do we determine the number of frequencies?
Frequency Hoppers have thousands of frequencies available.One real system may have up to 220 discrete frequency choices,randomly chosen on the basis of a code in combination with the information transmitted.
The number also depends on the systems error rate;for instance ,a library of 1000 frequencies could provide good operation when the interference or other noise is evenly distributed.
For a simple FH system the expected error rate is just J/N, where J equals the number of interferers with the power greater than or equal to signal power and N equals the number of frequencies available to the system.

## Slide 22: Contiguous & Overlapping Channel Spacing
It is usually assumed that the frequency hopping systems use the contiguous channel spacing; that is, the dehopped signal appearing at the receiver is not allowed to overlap from one channel into another. (This is not always true).
In many systems depending on the receiver used, transmit spacing can be such that significant overlap occurs .This overlap greatly reduces the RF bandwidth required for the transmitted spread spectrum signal.

## Slide 23: Time Hopping Systems
Time hopping ,in other words, is the pulse modulation. In this a code sequence is used to key the transmitter on and off. Transmitter on and off are therefore pseudorandom ,like the code, which can have an average transmit duty cycle of as much as 50%.

## Slide 24: Overview of Time Hopping Systems
There exists a fine difference between the time frequency hopping and plain frequency hopping .In the frequency hopping the transmitted frequency is changed at each code chip time ,whereas a time-frequency hopping system may change frequency only at one/zero transitions in a code sequence.
Simple time hopping modulation offers a little in the way of interference rejection. Due to the vulnerability to interference simple time hopping systems are usually combined with frequency hopping to prevent single frequency interferers from causing significant losses.
Time hopping systems find major applications in combination with frequency hopping systems. It may be used widely in ranging, multiple access and many other useful applications.

## Slide 25: Chirp Systems
Chirp systems are one type of spread spectrum modulation that do not necessarily employ coding but do use a wider bandwidth than the minimum required so that it can realize the processing gain.
Chirp transmissions are characterized by pulsed Rf signals whose frequency varies in some known way during each pulse period.The transmitted frequency swept signal is just that produced by a common laboratory sweep generator.
A dispersive filter(DDL) at the heart of a chirp receiver is a storage and and summing device that accumulates the energy received over an interval ,assembles it,and releases it in one coherent bursts.

## Slide 26: How does Dispersive filter work?
Let us assume that the transmitter sends a series of signals ,each of which is tagged in some manner. The receiver then sorts the signal according to their tags and assembles them so that they add together to produce a much stronger signal.
Actually, the tagging practice used by the transmitter is its frequency sweep which may be either high to low or vice versa, with each increment in frequency denoting a new signal to be sorted and stored.
The transmitted chirp signals has two parameters. Once these parameters are defined then the system performance is also defined. They are;
The frequency sweep |f2 – f1|=Δf.
The amount of time ΔT used to sweep the Δf band.

## Slide 27: Hybrid Techniques
The Hybrid combinations of modulation offer certain advantages as well as extend the usefulness of direct sequence and frequency hopping techniques.
The combination of two modulation techniques provides us with those characteristics which are not available from a single modulation technique.
The combinations often used are;
Simultaneous frequency hopping and direct sequence modulations.
Simultaneous time and frequency hopping.
Simultaneous time hopping and direct sequence modulation.

## Slide 28: Frequency Hopped /Direct Sequence Modulation (FH/DS)
This scheme consists of a direct sequence modulated signal whose center frequency hops periodically.
The spread spectrum signal shown is made up of a number of spread spectrum signals. A direct sequence signal covering a part of band appears instantaneously, and the entire signal appears in the other parts as dictated by frequency hopping pattern.

## Slide 29: How does the FH/DS system work?
If we need to design a RF spectrum of 1 GHz width. Then a system designer would specify 1136 Mcps code sequence generator to support a direct sequence transmitter , a frequency synthesizer with 200,000 five KHz spaced outputs for frequency hopping.
Now when we combine the frequency hopping and the direct sequence we could construct a signal that is 1GHz wide using 114 Mcps code sequence generator and a frequency synthesizer with only 20 50MHz spaced frequencies available.
Thus, if we compare the number mentioned above it is understood that 114 Mcps code sequence generator and 20 50 MHz frequency synthesizer could be readily constructed.

## Slide 30: FH/DS System
The FH/DS modulator differs from the direct sequence modulator mainly in the carrier frequency since the carrier frequency is varying rather than being constant.
The code sequence generator supplies code data to both frequency synthesizer to program its hopping pattern and to the balanced modulator for direct modulation.
In the receiver the local reference generator is essentially a replica of the transmitting modular , with two exceptions;
The local reference center frequency is offset an amount equal to the IF.
The DS code is unmodified by base band input.

## Slide 31: FH/DS System
The correlator used in the receiver is a superimposition of a direct sequence correlator on a frequency hopping correlator; that is, the local reference signal becomes a hybrid signal, which is then multiplied with all received input signals.

## Slide 32: Synchronism between FH and DS Code pattern
A synchronism between the FH and DS code pattern can be obtained when a given sector of DS code pattern is transmitted and the frequency channel remains the same.The DS code rate is normally much faster than the rate of frequency hopping.Therefore many chips of DS modulation occur in a single frequency channel.
Also the number of frequency channels are usually smaller than the number of code chips so that in a course of a complete code length all the frequency channels are used many times.

## Slide 33: Effect of interference on a FH/DS systems
When separated DS channels are used as access channels for multiplexing more than one DS signal on a frequency hopping carrier it is possible for a single frequency interfering signal to interfere with only one channel ,with no significant effect on the other.
To prevent the one user (or channel) being completely lost we need to change the order of the channel use periodically so that each user employs all the available frequencies equally and the effect of interference spreads over all the channels.
Thus, if a 20 channel system had an interfering signal in one channel ,it would be affected 1/20th time ,and if all the users shared that channel then it would be affected 1/400th time.

## Slide 34: Processing Gain of FH/DS system
The process gain of FH/DS system is given by;
Gp(FH/DS)=Gp(FH)+Gp(DS)
= 10 log(number of channels)+10 log(BW DS)/(R info)
For a 1GHz SS with the information rate as 5KHz for DSSS and 200,000 frequencies for frequency hopper the
Gp (DS)=10*log[(1*109)/(5*103)] =53dB
Gp(FH)=53dB
And for FH/DS system
Gp(FH/DS)=10*log20+10*log[(1*108)/(5*103)]=56dB.This increase in the Gp is due to the overlap allowed in the 20 100MHz wide channels.

## Slide 35: Time Frequency Hopping
Time Frequency hopping modulation has found its greater application in systems in which large number of users with widely variable distances or transmitted power are to operate simultaneously in a single link.
The general tendency is to design for the equivalent of a wireless telephone switching system in which random access and discrete address are the prime operational goals.
Such systems tend to employ simple coding ,primarily as addressing medium, rather than to spread the spectrum specifically.

## Slide 36: Overview of a near-far problem
Consider two receiving and transmitting links whose receivers and transmitters are spread such that the receiver for each link is positioned in a manner that the other link transmitter causes interference.

## Slide 37: Use of Time –Frequency Hopping
The anti jamming capacity of spread spectrum aids in such a situation but unfortunately is not enough under most conditions to overcome the disparity seen in the nearby and remote signals.
Processing to avoid fading is not the only answer to near-far reception difficulties. A much better solution is to time all the transmissions so that the desired and undesired transmitters are never transmitting at the same time.
With the time-frequency hopping the two transmitters can be programmed on different frequencies as well as at different times. Many links can then be operated at once if their time slots and frequency hopping channels are properly synchronized.

## Slide 38: Time Hopping Direct Sequence
When direct sequence transmission is used and code division multiplexing does not permit sufficient access to link, time hopping has proved to be useful way of adding time division multiplexing (TDM) to aid in traffic control.
All that is required to add time hopping TDM to a direct sequence system is the on-off switching and control.

## Slide 39: Switching Control in Time Hopping Direct Sequence
For the Time –hopping the on-off decision can be easily derived from the same code sequence generator used to derive the spectrum spreading code.
An easily implemented keying control would be an n-input gate which senses some previously chosen shift register state and turns the transmitter on or off at the appearance of that state.

## Slide 40: TH/DS System
A control signal would be used to block or enable the receiver front end synchronously with the expected transmit signal.
The direct sequence output would occur at pseudorandom intervals for a pseudorandom duration dictated by the code. This pseudorandom time division can permit more channel users, improve operation over simple code division multiplex and allow more access.

## Slide 41: Applications of different spread spectrum systems.
Area | Applications | Type of Systems | Primary User
Space Systems | Communications, multiple accessing, jamming protection | DS,FH. | Military
Avionics systems | Communications, position location, discrete addressing, low detectibility,jamming protection, | DS,FH, DS/FH, Chirp | Military
Test systems and equipment | Bit-error detection, non interfering in service, signal correlation, privacy. | DS | Commercial
Signal protection (nonmilitary) | Interference rejection, voice and data scrambling | DS | Commercial
Position Location | Collision avoiding, direction finding | DS | Many

## Slide 42: References
Spread Spectrum Systems- Robert C. Dixon (Second Edition)
Digital Communication-Edward Lee , David Messerschmitt (Second Edition)
Spread Spectrum Techniques-Robert C. Dixon (IEEE Press)
Spread Spectrum Communications-Edited by- Charles E. Cook, Fred W. Eller sick, Laurence B. Milstein, Donald L. Shilling (IEEE Press).