## Slide 1: CDMA AND GSM
BY
DEVEN INAMDAR
EE650

## Slide 2: Agenda
To study CDMA and GSM
Network Architecture
Interface Standards
Cell Structure
Channel
Modulation/Coding
Handoffs

## Slide 3: What is CDMA?
Channel sharing technique –Code Division Multiple Access
CDMA places all users onto the SAME frequency spectrum at the SAME time.
Concept uses a technique called Spread Spectrum (typ. Channel B.W is 1.23Mhz)
Intended to provide more Capacity than FDMA or TDMA

## Slide 4: Network Architecture-CDMA pg 19,fig 1-8

## Slide 5: Wireless Network Functions
Call Processing
Mobility Management
Supplementary Services
Radio Resource Management
Terrestrial Facility Management

## Slide 6: Call processing
Refers to steps required of both BSC and MSC to set up and release wireless calls
Functions includes Mobile Origination and Mobile Termination call set up and call clearing scenarios initiated by mobile, the BSC and the MSC.
Functions like Call failure scenarios, such as timer expiration and unsuccessful resource allocation are also included.

## Slide 7: Mobility Management
Procedures are needed to manage the registration and access status of individual mobile subscribers.
Management of mobile parameters such as mobile location, mobile identity, and authentication status in Visitor Location Register (VLR), and Home Location Register (HLR).
Also facilitates Roaming within or across networks deployed by other service provider.

## Slide 8: Supplementary Services
Include subscribers features that provide capability other than voice, such as:
Short Message Service (SMS)
Message Waiting Notification (MWN)
Call Forwarding and Call waiting

## Slide 9: Radio Resource Management
Refers to allocating radio channels for both voice and data traffic.
Also includes management of Handoffs within a BSC, between BSCs, and across MSCs.

## Slide 10: Terrestrial Facility Management
This function is contained in both BSC and MSC and it manages the terrestrial signaling links, routes and voice circuit resources.

## Slide 11: Call Processing Elements

## Slide 12: IS-95:
Published by Telecommunications Industries Association/Electronic Industries Association (TIA/EIA) for CDMA air interface.
Designed as a dual-mode operation, permits MS to operate in Advanced Mobile Phone System (AMPS) or CDMA environment
Uses the same 1.228 MHz bandwidth in every cell-frequency reuse factor = 1

## Slide 13: Cell Architecture IS-95

## Slide 14: IS-95 rates:
Defines two rate sets:
Rate set 1-operating at high rate of 8kbps..
Rate set 2-operating at high rate of 13kbps
The sets have different coding and syntax characteristics. The rates are negotiated between the mobile station and the network during connection set up and handshake.

## Slide 15: CDMA Timing operations
Precise timing required between Base Station and Mobile Station.
BS is responsible for providing this timing across the air interface, which is sourced from GPS. The GPS is traceable and synchronous with Universal Coordinated Time (UTC)
CDMA system time is the absolute time referenced at the BS, offset by the one-way or round trip of the transmission.

## Slide 16: Contd..
The intent of these operations is to ensure that the BS and MS are synchronized with regard to their TX and RX.

## Slide 17: IS-95 Channel Structure
The forward channels are divided into control and traffic channels, each channel identified by a specific WALSH CODE

## Slide 18: Orthogonal Spreading (OS) :
Here we apply an orthogonal Walsh codes (WC) W8 to W63 to the bit stream. W8 to W63 are used to identify each downlink traffic channel.
Full bit rate or the chip rate on air interface is 1.228Mhz which is the result of spreading the 19.2kbits/s I/P stream with 64 bit Walsh code. i.e. 19.2 x 64 = 1.228 Mbit/s
Results of WC operation are used as input to Quadrature spreading process

## Slide 19: Quadrature Spreading:
After O.S , each channel is quadrature spread with spreading sequence of length 2^15 which further codes the signal with PN seq. uniquely associated with a base station.
Two PN sequences are used, the I and Q quadratures.

## Slide 20: Contd..
3 types of control channels are used:
(a) one pilot channel
(b) one sync channel, and
(c) one to seven paging channels
On the Reverse Interface, channels consists of either Access channels or Traffic channel
Each Access channel is identified by a distinct access channel long code sequence
Each Traffic channel by distinct user long code sequence.

## Slide 21: Handoffs:
Refers to handoff of mobile station from one base station to another.
CDMA handoffs are characterized by beginning communications with new base station on the SAME freq. band before terminating with the old base station.
Types of Handoffs:
1. Soft Handoffs
2. Hard Handoffs

## Slide 22: Handoffs
Mobile is in communication with more than one BS and is making decisions about which BS to use, based on the signal strength.
Mobile station keeps an active set of BS in which a pilot channel is associated with forward traffic channel.
In Hard handoff, MS abandons one BS and then picks up another. Only one BS is in active set-”break before make”.

## Slide 23: Figure:

## Slide 24: GSM:
Global System for Mobile Communication.
Operates typically in 3 bands; GSM 900, GSM 1800, GSM 1900 (PCS 1900) and also GSM 850
900 is the original system that was FIRST implemented in Europe in early 80’s.

## Slide 25: GSM- Air Interface (Um)
Um interface uses a combination of FDMA and TDMA
124 channel pairs operate at full duplex (FDX) with the uplink and downlink allocated with different carrier frequencies. Thereafter, these FDM channels use TDMA.
TDMA slots are allocated with 8 slots to a frame and include information and control bits.

## Slide 26: Contd..
Each individual slot comprises of 156.25 bits with a slot time 0.577ms.
User receives 114 bits from this slot, and remaining bits are used for synchronization and control functions.
The instance of one time slot makes up one physical channel as shown in the figure

## Slide 27: Figure:

## Slide 28: Authentication:
GSM uses Authentication Algorithm called A3, which is contained in removable SIM or Subscriber Identity Module chip.
SIM card contains a microprocessor that can store different authentication programs for different system operators.
The authentication process is carried out using shared secret data value called ‘Ki’. It is stored in both the mobile and authentication center of base cellular system.

## Slide 29: Process:

## Slide 30: Traffic channel structure:
GSM uses a single radio carrier frequency waveform to multiplex (time-share) control, voice and data channels.
GSM conversation uses radio channel called a Traffic Channel (TCH).
A frame is composed of 8 time slots used by 8 different conversation. From each frame, each user is assigned to a particular time slot burst for reception, and a particular corresponding burst for transmission.

## Slide 31: Figure

## Slide 32: Contd..
Voice comm. is conducted on two 200kHz wide modulated carrier frequency waveforms: a downlink or forward carrier (from cell site to the mobile to mob. Telephone) and an uplink or reverse carrier (from mobile phone to cell site).
GSM systems allow several users to share each radio channel frequency by dedicating a specific time slot from each frame to the users.

## Slide 33: Contd..
Voice channels can be FULL rate or HALF rate . Full rate systems assign one time slot per frame and allow 8 users to simultaneously share a radio channel. Data rates for users are 22.8 kbps, but typ. 9.6kbps for customer data or fax communication.
Half rate GSM systems assign one time slot every other frame to allow up to 16 users to share a radio channel. Here user available data rates are11.4kbps.

## Slide 34: Radio channel BW and Spacing:
Nominal bandwidth of modulated GSM carrier frequency is 200kHz.
GSM uses a special form of FSK which has low amount of adjacent frequency spectrum power emission.
Spectrum shows that radio energy is primarily distributed within 200kHz band.

## Slide 35: Spectrum:

## Slide 36: Modulation and Data rates:
GSM uses Gaussian Minimum Shift keying or GMSK modulation to produce a gross data transmission rate of 270kbps.
Objective of GMSK was the optimum or near optimum combination of several desirable properties which include small susceptibility to radio noise & interference, small bandwidth and constant power level.
The total data rate achieved is shared by multiple users on a single radio carrier channel.

## Slide 37: Contd..
After discarding the non-information bits, actual assigned bit rate that a subscriber gets to use in each time slot is only 22.8kbps.
Because of fading, interference noise etc.., a portion of this gross delivered bit rate is devoted to data bits used to detect and correct bits that are in error. Hence,
For GSM digital speech coder, only 13 kb/s of 22.8 kb/s is ‘Real’ data.

## Slide 38: References:
‘GSM Superphones’ by Lawrence Harte, Richard Levine & Geoff Livingston.
‘CDMA Internetworking’ by Su-Lin Low, Ron Schneider
‘Mobile and Wireless Networks’ by Uyless Black.