## Slide 1: CDMA1X vs WiFi/WiMAX
An overview of Broadband Technologies in the U.S.

## Slide 2: CDMA basic concepts
800MHz and 1.9GHz bands
1 bit of conversation = 128 coded bits
Orthogonal Signals due to Walsh codes
Spread Spectrum through PN codes
Power Control for near-far effect
QPSK modulation
CDMA channels limit by tolerance to interference
Interference from other cell-site users as Gaussian noise
Shannon limit
RAKE receiver for multi-path
Notes: Encoder 2x output
Output of encoder rep 64 times
Xored with WALSH code (id call)
Xored with PN to id sector
Mod to 800MHz carrier freq
Number of users M = 1.45*Gp (processing gain)
Shannon limit says CDMA systems can have more users per cell than traditional narrowband systems limited by number of dimensions,
But have to account for interference noise and power control accuracy, which lowers this value

## Slide 3: CDMA
Simplified Block Diagram

## Slide 4: CDMA
A/D and Vocoder
Notes: Takes advantage of moments of silence in speech

## Slide 5: CDMA
Encoder/Interleaver

## Slide 6: CDMA
Interleaving Method

## Slide 7: CDMA
Walsh and PN codes Applied

## Slide 8: CDMA
Quadrature Spreading

## Slide 9: CDMA RAKE Receiver
Multi-Path Advantage

## Slide 10: CDMA Block Diagram

## Slide 11: Walsh Functions
Functions used as spreading code Forward Channel
Used to form orthogonal modulation symbols on Reverse Channel
64 mutually orthogonal functions
Digital Speech multiplied by Walsh
At Receiver, mulitplied by synchronized Walsh function for i-th user (differentiate users)
Notes: to extract desired call at receiver and differentiate between rest of users since rest of them look like noise at receiver

## Slide 12: PN (Pseudorandom Noise) Sequences
PN sequence is Modulo-2 Added to Data:
0  1 and 1  -1
Data Sequence: s(t)
Code Sequence: c(t)
At Receiver, Modulo-2 Added with Code
s(t) | -1 | -1 | 1 | -1
c(t) | -1 | 1 | 1 | -1
s(t)c(t) | 1 | -1 | 1 | 1
s(t)c(t) | 1 | -1 | 1 | 1
c(t) | -1 | 1 | 1 | -1
s(t)c(t) c(t)=s(t) | -1 | -1 | 1 | -1
Notes: Deterministic, periodic
Uses feedback shift registers

## Slide 13: CDMA2000 Rel. A
Uses cdmaOne overhead channels
Adds new overhead channels
Support for higher speed data
Capacity improvements
Better support for packet-switched services
CDMA1X EV-DO (Verizon V-Cast) 3.1Mbps down-link
2.1Mbps Uplink
WWAN
Mobile data and Voice
Notes: Phase 2 EV-DV for voice and data on same carrier w/ rates up to 4.8Mbps

## Slide 14: The ‘Wi’ Technologies
OFDM-based broadband solutions

## Slide 15: Wi-Fi (802.11)Standard
Used for LAN (local area networks)
<300 ft range
Theoretical data rate ~<11Mbps (with limitation of ADSL/cable speed)
Spectrum at 2.4GHz (vulnerable to devices operating at same frequency)
Not capable of seamless hand-offs
Not a replacement to cellular broadband solutions
Notes: Wireless fidelity
Cord-less phones, microwave interference
1250 Wi-Fi hotspots to cover area of 1-mile radius cell-tower
Standalone hotspot business model not lucrative – even T-Mobile says revenues inconsequential

## Slide 16: Wi-MAX (802.16) Standard
Used for MAN (Metropolitan area networks)
<30 mile range
Theoretical data rate ~<100Mbps
Spectrum allocation at 2.5GHz for US/Mexico/Brazil
Needs high-gain antennas size of laptops
For Max Range, needs tall towers and unobstructed LOS
Not a replacement to cellular broadband solutions
Notes: World-Wide Interoperability Microwave Access
Variant offered for limitted mobility (walking/slow speeds) but no model available yet and skepticism
High frequency causes need for many towers and high power to send signal further distances
Can be used as cell-site backhaul, wifi backhaul, rural broadband

## Slide 17: FLASH-OFDM
WWAN type technology
Average data rate ~1.5Mbps
Provides mobility and QoS (Quality of Service)
NLOS capable
Requires 1.25MHz of paired spectrum
Current trials operate in 700MHz, 800MHz, and 2.3GHz bands
Can be paired with CDMA standard
Notes: Similar attributes to CDMA
Most likely what will happen since Qualcomm now owns Flarion – devloper of FLASH-OFDM

## Slide 18: OFDM modulation
Orthogonal Frequency-Division Modulation
Data is 1st modulated in QAM or QPSK
Truly orthogonal channels (harmonically-spaced frequency channels)
Reaps benefits of spread spectrum (with frequency-hopping)
Reaps benefits of TDMA-type technologies with little interference from adjacent channels

## Slide 19: OFDM
Notes: How the tones are orthogonal – 0’s at each-other’s frequencies other than their own

## Slide 20: OFDM Transmitter Chain
Notes: Cyclic prefix for channel effects – must be long enough for this to fade

## Slide 21: Time Varying Fading

## Slide 22: OFDM Channel Resource

## Slide 23: Time/Freq Representation of OFDM

## Slide 24: OFDM Illustration
First set of BPSK data:
1, 1, -1, -1, 1, 1, 1, -1, 1, -1, -1, -1, -1,
-1, 1, -1, -1, -1, 1, 1, -1, -1, -1, 1, 1,…
Serial to Parallel (assume 4 carriers):
1st N pts to IFFT
2nd N pts to IFFT
3rd N pts to IFFT
etc.

## Slide 25: OFDM Illustration (cont.)
We ‘pretend’ to be in Frequency Domain:

## Slide 26: OFDM Illustration (cont.)
FFT equation:
IFFT equation:

## Slide 27: OFDM Concept
Essentially, IFFT or FFT multiplies each symbol by sinusoid at particular carrier frequency (we map)
Since spacing between carriers are harmonics, orthogonal
Best option for frequency-selective fading channels (sinusoids are eigenfunctions of channel)

## Slide 28: OFDM Concept
BPSK data:
Each symbol sent on carrier:

## Slide 29: OFDM Matlab example
Data stream (16-QAM modulated):
Send through IFFT (output of IFFT)
Add cyclic prefix for every frame
(last 31 symbols appended to front)
Transmit

## Slide 30: Matlab example (cont.)
Constellation at Receiver using Cyclic Prefix and Preamble
Notes: CDMA1X EV-DV Rel. B will be OFDM-based

## Slide 31: References
Garg, Vijay K. IS-95 CDMA and cdma2000 Cellular/PCS Systems Implementation, Prentice Hall, 2000.
Teets, Gregory J. A.G. Edwards, Wireless Technology: WiFI & WiMAX, August 6, 2004.
Aytar, Ozgur. Pyramid Research, Positioning WiMAX How WiMAX Stands Up To DSL, Cable, Wi-Fi and 3G.
Paolini, Monica. Wi-Fi, WiMAX and 802.20 – The Disruptive Potential of Wireless Broadband. BWCS Ltd, 2004.
Flarion Whitepaper Vector-LDPC™ Codes for Mobile Broadband Communications
OFDM On-Line Tutorial: http://www.complextoreal.com/chapters/ofdm2.pdf
Qualcomm CBT CDMA Concepts Training CD.
Flarion Whitepaper OFDM for Mobile Data Communications
Liu, Ke; Kadous,Tamer and Sayeed, Akbar M. IEEE TRANSACTIONS ON INFORMATION THEORY, Orthogonal Time–Frequency Signaling Over Doubly Dispersive Channels, Vol. 50, No. 11, November 2004.
Belk, Jeffrey K. Why MAX? A Wireless Primer and Discussion on Wireless Reality. http://www.qualcomm.com/enterprise/pdf/WhyMAX_JBelk.pdf