## Slide 1: Data Hiding In Digital Images
Kim Leung
James Thammarath
SDSU EE657 Fall 2005

## Slide 2: Data Hiding
Steganography
  The art of concealed communication
  The very existence of the concealed message is a secret
Watermarking
  The practice of hiding data within a file
  The hidden message is imperceptible whether its existence is known or unknown

## Slide 3: Steganography
Technique of concealing the existence of hidden information
Typically, relates covert point-to-point communication between two parties
Allows a large amount of data to be embedded but with limited robustness
The secret message is embedded in a cover image using a stego-key, resulting in a composite image called the stego-image
The stego-image must be as identical as possible to the original so that the presence of the information will be undetectable

## Slide 4: Steganographic System
Embedder
Extractor
Cover Image
Secret Image
Stego-Image
Extracted
Secret Image
Stego-Key

## Slide 5: Watermarking
Similar to Steganography in many aspects but boosts the requirements of robustness
Embeds an amount of information that cannot be removed or altered without resulting in the cover object being entirely unusable
Limited data capacity, highly robust and totally resistant to distortion when under attack

## Slide 6: Watermarking Terminology
Visible Watermarks
  Visual patterns which are inserted into or overlaid on images
Fingerprinting
  Special applications of watermarking where information specifying the creator or recipient of digital data is embedded as watermarks
Labeling
  Watermarking where the embedded data may contain any information of interest, such as a unique data identifier

## Slide 7: Terminology (Continued)
Bitstream Watermarking
  Watermarking of compressed data such as compressed video
Fragile Watermarks
  Watermarks that have only very limited robustness applied to detect modifications of the watermarked data

## Slide 8: Watermarking Applications
Identification of copyright owner
Copyright protection of content
Image authentication
Transaction tracking
Copy control
Device control

## Slide 9: Image Authentication Example Using A Fragile Watermark

## Slide 10: Watermark Properties
Imperceptible
  Does not detract from the aesthetics of the image
Inseparable from embedded image
  Is not removed when the image is displayed or converted to different formats
Undergoes the same transformations as the embedded image
  Sometimes possible to determine what transformations have been applied to the image by looking at the watermark
Robustness

## Slide 11: Watermarking System

## Slide 12: Informed Detection

## Slide 13: Blind Detection

## Slide 14: Data Hiding In The Spatial Domain
Bit decomposition of a 4x4 8-bit gray scale image
Original image is decomposed into 8 bit planes where b0 is the LSB
In an RGB image, each bit plane pixel holds 3 bits representing red, green, and blue

## Slide 15: Least Significant Bit (LSB) Method
Most common technique for hiding data in the spatial domain
Involves replacing the N least significant bits of each pixel of a container image with the N most significant bits of the hidden image
The key used by the encoder and decoder is the number of bits N that was replaced
Provided that the number of bits replaced in the container image is kept reasonably low, alteration to the image will be imperceptible to the human eye

## Slide 16: LSB Method (Continue)

## Slide 17: LSB Method Example
The result of replacing successive bit planes with random data. The original image is at the top left. The bottom left image results after 7 bit planes have been replaced with random data.

## Slide 18: LSB Method Example
The result of replacing successive bit planes with ASCII text data. The original image is at the top left. The bottom left image results after 7 bit planes have been replaced with ASCII text data.

## Slide 19: Spatial Domain Methods Pros & Cons
Pros
  Low complexity
  A large quantity of embedded data can be included in even the most modestly sized images
  Good for Steganography due to its high capacity
Cons
  Robustness limits overall effectiveness
  Any attack, noise distortion, alteration, or compression of the composite image will damage the embedded data
  Cannot be used for watermarking due to its limited robustness

## Slide 20: Data Hiding In The Transform Domain
Also known as sub-band decomposition techniques
Transforms the cover image into another domain before embedding
After embedding, the composite image is recovered by applying the inverse transform
Serves as a stronger channel for transmitting information covertly while minimizing distortion of container image

## Slide 21: Discrete Cosine Transform (DCT)
The classic and most popular domain for image processing
Full-Image DCT or Blockwise DCT
Horizontal frequencies increase from left to right
Vertical frequencies increase from top to bottom
The 64 basis functions of an 8x8 matrix

## Slide 22: DCT Embedding
Data embedded in the high frequency bands are subject to removal through compression and distortion from noise
Data embedded in the low frequency bands may be more noticeable because low frequency bands contain the perceptually important aspects of the image
Dr. Ingemar J. Cox proposed a method, Spread Spectrum Watermarking, arguing that the perceptually significant components have a perceptual capacity that allows watermark insertion without perceptual degradation

## Slide 23: DCT Spread Spectrum
Watermark structure should be constructed as an independent and identically distributed (i.i.d.) Gaussian random vector
Embed in the perceptually most significant component spectrums in a spread spectrum type fashion
Low false positive and false negative detection
Uniform spread of watermark energy in the pixel domain

## Slide 24: DCT Spread Spectrum
D : each document
V= : seq of D to be inserted by wmk
X= : watermark to be inserted
V’= : watermarked sequence
D’ : watermarked document
: attacked document
: attacked watermarked seq of
: attacked watermark

## Slide 25: DCT Spread Spectrum Method Pros & Cons
Pros
  Robust against common signal and geometric processing operations.
  Robust against attacks
  Applicable to audio, image and video data
Cons
  Need to synchronize with the unmarked image in the decoder
  Limited embedding capacity

## Slide 26: Discrete Fourier Transform (DFT)
Data is put into the magnitude or phase parts of the DFT coefficients
Modifying the phase coefficients will have less of a visual impact than modifying the magnitude coefficients
The phase component is also more robust against noise distortion

## Slide 27: Circular Watermarking Method
Developed by Dr. Vinicius Licks of the University of New Mexico
A matrix, with size equal to the DFT, is initialized to zero
The secret data is applied to this empty matrix in a ring shape with radius r and magnitude α, which are the keys to the embedder and extractor
In forming the ring, the data is duplicated 4 times, once for each quadrant
At the pixels where the data bit ‘0’ has been embedded, the DFT value is reduced by α/10 to minimize the chance that the value will be decoded as a ‘1’
In the extraction process, the pixel values at the 4 locations are averaged together

## Slide 28: Discrete Wavelet Transform (DWT)
decomposes an image into blocks that comprises of a lower resolution approximate image (A), and horizontal (H), vertical (V), and diagonal (D) detail components
More accurately models aspects of the Human Visual System (HVS) as compared to DCT or DFT
2-level 2D DWT
A1 H1 D1 V1
A2 H2 D2 V2
Original Image
The four bands are usually referred to as LL (A), LH (V), HL (H), and HH (D) bands, where the first letter represents the filter used on the rows and the second letter represents the filter used on the columns with L being a LPF and H being a HPF

## Slide 29: DWT Embedding
Developed by Chae and Manjunath from the University of California, Santa Barbara
Able to embed an image that is 25% the size of the cover image
Informed detection system
Robust against JPEG compression and low pass filtering

## Slide 30: Summary Of Techniques
 | LSB | DCT | DFT | DWT
Capacity | High | Limited | Limited | Limited
Imperceptibility | Good | Fair | Fair | Fair
Robustness | Poor | Good | Good | Good

## Slide 31: References
J.J. Chae, B.S. Manjunath, “A Robust Embedded Data from Wavelet Coefficients”. Department of Electrical and Computer Engineering University of California, Santa Barbara.
I.J. Cox, J. Kilian, F.T. Leighton, and T. Shamoon, “Secure spread spectrum watermarking for multimedia” in IEEE Transactions on Image Processing, vol: 6 Issue: 12, Dec. 1997, pp:1673-1687
I.J. Cox, M.L. Miller, J.A. Bloom, Digital Watermarking. Morgan Kaufmann Publishers, San Francisco. 2002.
R.C. Gonzalez, R.E. Woods. Digital Image Processing. Second Edition. Prentice Hall, New Jersey. 2002.
R.C. Gonzalez, R.E. Woods, S.L. Eddins. Digital Image Processing Using Matlab. Second Edition. Prentice Hall, New Jersey. 2004.
S. Katzenbeisser, F.A.P. Petitcolas, Information Techniques for Steganography and Digital Watermarking. Artech House, Boston/London. 2000
E.T. Lin, E.J. Delp, “A Review of Data Hiding in Digital Images”. School of Electrical and Computer Engineering Purdue University.
X. Niu, Z. Lu, S. Sun, “Digital Watermarking of Still Images with Gray-Level Digital Watermarks” in IEEE Transactions on Consumer Electronics, vol: 46 No. 1, Feb. 2002, pp:137-145
homepages.cae.wisc.edu/~yhwang/ece738/presentation_.ppt
homepages.cae.wisc.edu/~iychung/ ECE738/Multimedia%20Watermarking%20Techniques_2.ppt
http://books.elsevier.com/us//mk/us/subindex.asp?maintarget=companions/defaultindividual.asp&isbn=1558607692&country=United+States&srccode=&ref=&subcode=&head=&pdf=&basiccode=&txtSearch=&SearchField=&operator=&order=&community=mk
http://www.owlnet.rice.edu/~rwagner/steg.html#intro
www.mathworks.com